## Slide 1: Occupational Lung Disease and Respiratory Protective Equipment Awareness
Disclaimer: We want to prevent long-term occupational lung disease from occurring. All guidance herein is provided in good faith and Step Change in Safety nor its member companies accept responsibility for any inaccuracies or omissions contained within this safety moment.

## Slide 2: For Info
This pack contains information on Occupational Lung Disease and Respiratory Protective Equipment (RPE).
The pack is not suitable for start to finish presentations in a safety meeting.
We designed the topics to be standalone.
We encourage you to:
Select the ones most relevant to your team and/or activities
Use one or two slides/ or films for your safety meetings
Use them as individual toolbox talks or pre-shift briefings
Please share your feedback & own incident learnings
Feedback using the enquiry form: https://www.stepchangeinsafety.net/contact/
Share Learnings: https://www.stepchangeinsafety.net/alerts-moments/submit/
Thanks for playing your part
Occupational Lung Disease Awareness
Please be nice to your colleagues.
No one wants this on their death certificate…
“Death by PowerPoint”

## Slide 3: Did you know?
Use a Toolbox Talk to ensure your team understands the hazards, the harm they can cause us, and how we can control them.
At the time of the Toolbox Talk check if tight-fitting RPE is required, and if it is required are the wearers clean shaven.
When we talk about respiratory protective equipment the users’ health is the top priority.
We can prevent potential long term health issues to ourselves and colleagues by rectifying and reporting any unwanted conditions we observe. Reporting unwanted conditions allows our organisation to act on them and communicate any applicable learnings.
*12,000 lung disease deaths each year are estimated to be linked to past exposures at work
It is the duty of employers to either prevent exposure or, where this is not reasonably practicable, adequately control exposure by applying protection measures appropriate to the activity and consistent with the risk assessment
Most occupational lung diseases can be prevented or limited by the correct use of respiratory protective equipment (RPE)
COSHH Approved Code of Practice requires wearers of tight-fitting respirators to be face fit tested by a competent person
Many workers:
Are not provided with the correctly selected respirators
Are no provided with correctly maintained respirators
Do not wear their respirators properly
This can lead to exposure to hazardous substances affecting their health
*Health and Safety at Work Summary statistics for UK 2023

## Slide 4
Prevention of Occupational Lung Disease
Don’t Risk Your Long -Term Health
What hazardous substances might you come into contact with at site and how?
Introduction to Respiratory Protective Equipment
Film provided by Stork and edited by Step Change in Safety
Click here or scan QR code to watch interactive film with questions

## Slide 5
The hazardous substance and the amount in the atmosphere (exposure)?
The form of the substance in the air (fumes, fibres, mists, solvent vapours, dusts and gases)?
Type of task being carried out?
Any specific wearer requirements, such as clean-shaven compatibility, other items of PPE such as safety eyewear, fall arrest equipment, etc
Are you compliant with the site’s regulatory requirements?
Respiratory Protective Equipment (RPE)
Where an inhalation exposure risk remains after other reasonable controls have been put in place, the RPE selected must be adequate and suitable.
Is your RPE adequate and suitable for:
Adequate – It is right for the hazard and reduces exposure to the level required to protect the wearers health.
Suitable – It is right for the wearer, task and environment, such that the wearer can work freely and without additional risks due to the RPE.
Respiratory Protective Equipment & Risk Assessment
Film provided by Stork and edited by Step Change in Safety
Click here or scan QR code to watch interactive film with questions

## Slide 6
Types of Respiratory Protective Equipment

## Slide 7
Task related factors to consider -
Work rate: higher work rates are associated with increased breathing and sweating, which can affect the performance of some types of RPE. Increased breathing rate can cause contaminants to leak inwards, and sweating can cause facepieces to slip.
Wear time negative: pressure tight fitting masks are commonly seen as being uncomfortable to wear for long periods of time. The HSE Guidance recommends wearing negative pressure masks for under 60 minutes, mainly to reduce the risk of fatigue.
Abnormal temperature or humidity: in hot or humid conditions, wearing negative pressure RPE increases heat stress, sweating, and discomfort.
Vision: If workers need to wear eye protection when wearing negative pressure masks a common issue is the misting of the eye protection due to heat build-up inside the mask.
Communication: all RPE will affect the user’s ability to communicate, in certain circumstances, employers should consider providing communication devices.
Congested work areas: if congested work spaces cannot be avoided, back mounted PAPR can sometimes be bulky and a snagging hazard.
Mobility: if the user needs to move from one location to another.
Wearer related factors to consider:
Headwear: any items worn on the head for safety or religious reasons can restrict the choice of RPE.
Facial hair: anyone with facial hair is always pushed towards using loose-fitting facepieces that do not rely on a tight seal.
Medical conditions: anyone wearing a respiratory should be physically fit, anyone who suffers from respiratory disorders would benefit greatly from wearing powered air units.
Choosing the Appropriate Respiratory Protective Equipment (RPE)
The decision on choosing appropriate respiratory protection should be based on the overall analysis of the specific factors and not on protection factors alone.

## Slide 8
Face Fit Testing
According to the requirements laid out in the Health & Safety Executives guidance note INDG 479 and HSG53 care must be taken to ensure that respirators fit perfectly.
Which masks need to be tested?
Disposable half masks
Re-usable filter or cartridge half masks
Powered respirators (Tight Fitting)
Full face filter or cartridge masks
Full breathing apparatus masks
.
How do I fit my mask correctly?
How do I fit my mask correctly?
How do I fit my mask correctly?
Who can carry out a face fit test?
A competent person should carry out a face fit test. Competency can be proven by accreditation to the BSIF Fit2Fit Fit Testers Accreditation Scheme, however, this is not compulsory.
“In preparing the Fit2Fit RPE fit testers accreditation scheme, BSIF, and other industry stakeholders have worked closely with the experts in Health and Safety Executive (HSE). But if you follow this scheme, you will be doing enough to demonstrate good practice.”

## Slide 9
How Does Facial Hair Effect the fit of a mask?
Video provided by JSP Safety
Facial hair is known to interfere with the sealing surface of the mask to the wearer.
A recent study by the Health and Safety Executive (RR1052) on the effect of stubble growth on the protection given by filtering facepieces and half masks, showed that protection could be significantly reduced where stubble was present, beginning within 24 hours from shaving, and generally worsening as facial hair grew.
In order to align with COSHH, HSE advises that the individual should be clean shaven where the RPE seal meets the face.
RPE is essential for safeguarding the wearer from hazardous substances. The effectiveness however depends on a proper fit to the face.
RPE can’t protect the wearer if it leaks, and a major cause of leaks is the poor fitting of RPE.
Facial Hair Fit Factors – How does facial hair affect half mask fit?

## Slide 10
Face Fit Testing and Pre use checks – Good Practice
Respiratory Protective Equipment Which Requires a Facial Seal
Film provided by Stork and edited by Step Change in Safety
Purpose of RPE is to filter out harmful contaminants and provide the wearer clean air to breathe
If you do not shave or remove piercings, you are in danger of breathing contaminated air
Click here or scan QR code to watch interactive film with questions

## Slide 11
Pre use inspection of face pieces
Film provided by Stork and edited by Step Change in Safety
RPE should be inspected prior to each use
Click here or scan QR code to watch interactive film with questions

## Slide 12
Before wearing RPE – Ask yourself……..
Film provided by Stork and edited by Step Change in Safety
Have you been face fit-tested for the mask being used?
Is it being worn correctly?
Are you clean shaven before using the mask?
Have you been trained to put on and check the mask?
Is the mask being stored correctly?
Is the mask in good condition?
Are filters in place and in date?
If you are using an air fed RPE, has the air quality been checked?

## Slide 13
Text and images taken from leaflet:
What do you know about dust? Scan the QR code to learn more.
Why is Respiratory Protective Equipment (RPE) important?
12,000 People die each year from occupational lung diseases linked to past exposures at work.
That’s 12,000 families devasted simply because their loved one went to work and was not sufficiently protected.
With occupational lung diseases, it might not be right away; many of the 12,000 deaths are linked to past exposure to asbestos, but it is now that their lives, and families’ lives, are impacted. It could take years for affects to become apparent, so it is important to protect yourself every day.
The Hidden Killer – Jean Morgan’s Story
Jean’s husband Christopher was diagnosed in November 2008 with mesothelioma – an incurable cancer caused by exposure to asbestos.
Here Jean movingly describes how Christopher’s diagnosis has impacted on their family and their lives

## Slide 14: Useful Resources and References
HSE – COSHH Guidance
HSE – COSHH Approved Code of Practice and guidance
HSE - INDG479 Guidance on Respiratory Protective Equipment fit testing
HSE – HSG53 Respiratory protective equipment at work – A practical guide
HSE – Managing and working with asbestos – Control of Asbestos Regulations 2012 – ACOP & Guidance
HSE – Control of lead at work (Third edition)
TRAC – COSHH Awareness presentation
Recording and presentations – Occupational Lung Disease & RPE event – 6th Nov 2024
*Health and Safety at Work Summary statistics for UK 2022